## Slide 1: Behavior-based predictive safety analytics, CMV Naturalistic Data
Technology transfer

## Slide 2: Behavior-based predictive safety analytics
The prediction of road crash involvement based on individual driver behavior characteristics (“finding the unsafe drivers”)
Key applications in fleet management and insurance, but also in evaluating safety benefits of automated driving
Predictive safety analytics traditionally based on relating conviction/violation records to crash involvement
Naturalistic driving (ND) data enables relating behavioral indicators of individual drivers to crash involvement
This requires (ND) datasets containing both “normal” driving behavior and a large number of crashes
In addition to existing public-funded ND studies (e.g., SHRP2), commercially collected ND data (e.g., Lytx and SmartDrive) yields potentially huge data sets with thousands of crashes

## Slide 3: Behavior-based predictive safety analytics model
Personality / lifestyle / cognitive style
Subjective self-rating of driving style
Sociocultural
factors
Behavioral interventions
Crash involvement
Behavioral history
Observable driving behavior

## Slide 4
Naturalistic Data Foundations
Naturalistic data contain numerous variables to use for analysis
Notes: Study-dependent questionnaires, often including demographics or other evaluative criteria

## Slide 5: Analysis of CMV Naturalistic Driving Studies
Two general types of naturalistic driving (ND) data that can be utilized
  Continuous data, much of which has been collected in previous federally sponsored projects and is available for reanalysis;
    Systems provide camera views, GPS data, and various data elements from the vehicle network, including data from any active safety systems installed on the truck
    Data are collected and stored for all reduction and analyses
  Event-based OBMS data collected by fleet/driver management companies as part of driver behavior management services offered to vehicle fleets.
    Systems typically provide camera views, GPS data, and various data elements from the vehicle network, including data from any active safety systems installed on the truck
    Events are triggered by kinematic or other sensory signals
    Continuous vehicle network data are not available outside of the events

## Slide 6: VTTI-collected Naturalistic Continuous Databases Overview
Dataset Title | Trucks | Buses | Drivers | Miles | Collection System
FAST DASH 1 | 19 | 0 | 21 | 1,336,635 | NextGen
FAST DASH 2 | 17 | 0 | 27 | 1,450,000 | NextGen
Onboard Monitoring System (OBMS): Motorcoach | 0 | 44 | 73 | 1,141,037 | NextGen
Onboard Monitoring System (OBMS): Truck | 206 | 0 | 167 | 2,483,332 | NextGen
Crash Avoidance System (CAS) FOT | 150 | 0 | 169 | 3,245,000 | MiniDAS
Canadian Truck Study | 25 | 0 | 25 | 934,292 | NextGen
FAST DASH 4 | 15 | 0 | 15 | 220,000 | NextGen
Heavy Vehicles
Dataset Title | Drivers | C/NC | Baseline | Miles | Collection System
SHRP2 | 3,542 | 8,758 | 32,581 | 35,000,000 | NextGen
Light Vehicles
There are multiple publicly available continuous naturalistic driving databases available collected by VTTI over the previous decade
Data Collection Roadway Example

## Slide 7: Opportunities for CMV Naturalistic Data

## Slide 8: Opportunities for CMV naturalistic data
Behavioral indicators can be created using naturalistic continuous driving data
  Typically kinematic triggers which include, but are not limited to:
    Speeding
    Following Distance
    Longitudinal Acceleration/Deceleration
    Lateral Acceleration
    Lane Deviation
    Steering
Examples are provided on the following slides

## Slide 9
Speed limit
Road Segment 1
Event 8
Event 7
Event 6
Event 5
Event 4
Event 3
Event 2
Event 1
Vehicle speed
Average speed per Road Segment
+20 mph
+15 mph
+10 mph
+5 mph
Speed Limit
-5 mph
-10 mph
-15 mph
Speed Behavior
Time
Speed Behavior Example
Road Sgmt 2
Road Sgmt 3
Road Sgmt 4
Road Sgmt 5
Road Sgmt 6
Road Sgmt 7
Legend

## Slide 10: Following Distance Examples
Event 1
Event 2
Event 3
Event 4
1-2s
2-3s
3-4s
< 1s

## Slide 11: Longitudinal Deceleration Examples
Event 1
Event 2
Event 3
-0.1g to -0.2g
<(-0.3g)
-0.2g to -0.3g

## Slide 12: Lateral Acceleration Examples, Left or Right
Event 1
Event 2
Event 4
0.1g to 0.2g
>0.4g
0.2g to 0.3g
Event 3
0.3g to 0.4g

## Slide 13
GPS
Road Segment ID
Street Name
Controlled Access
Ramp
Paved
Time Zone
Divider
Intersection
Lane Category
Grade Category
Speed Limit
Traffic Sign
etc.
Opportunities for CMV naturalistic data
Roadway attributes can be utilized

## Slide 14
  Identification of inattention and unsafe driver behaviors
  Examine prevalence of driver distraction in commercial trucks and buses
  Analyze risks associated with performing various tertiary tasks.
Opportunities for CMV naturalistic data

## Slide 15
Machine Vision
  Internal
    Face/Eye tracking
    Heat-based tracking
    Distraction
  External
    Vehicles
    Pedestrians
    Roadway
    Environmental Conditions
Opportunities for CMV naturalistic data

## Slide 16
Automation algorithms can be created to replicate how advanced driver systems may be implemented or advanced driver assist systems may be triggered
Opportunities for CMV naturalistic data

## Slide 17
Additional data matching can be conducted
Potential data to match with naturalistic data
  Cell phone records (SHRP2)
  ELD Data
  Driver Monitoring Systems
  Driver Activity
  Carrier Crash Information
  CSA/MCMIS information
Opportunities for CMV naturalistic data

## Slide 18
Crash events can be generated based on naturalistic data
  Crash
  Near-crash
  Breakdown by crash parameters
Opportunities for CMV naturalistic data
Chart: Different types of Safety related events per 1,000,000 VMT
| CRC, FD1 | CRC, FD2 | CRC, OBMS | NC, FD1 | NC, FD2 | NC, OBMS | Crashes, PDO+ FMCSA | Crashes, FD1 | Crashes, FD2 | Crashes, CAS FOT
 | 164.67 | 78.5857 | 409.5036 | 47.05 | 36.7848 | 130.1123 | 1.546 | 1.38 | 5.8521 | 0.9245
Conflicts
Crashes

## Slide 19
Typical CMV crash rates use 100 million vehicle miles traveled (VMT) as the exposure
  Involvement of large trucks (per 100m VMT) in:
    fatal crashes: 1.56
    injury crashes: 35.9
    property damage only (PDO) crashes: 122.1
Naturalistic continuous data is not to that point (yet)
Naturalistic event-based data contains billions of VMT
FMCSA Truck and Bus Crash Facts, 2017 (May 2019)
Opportunities for CMV naturalistic data

## Slide 20: Barriers in CMV Naturalistic Data

## Slide 21: Barriers in CMV naturalistic data
Continuous data barriers
  Driver samples are typically limited in number, even when compared with light vehicle continuous naturalistic data
  Data are often collected with research objectives in mind
  Storage of vehicle network and other time series data is cumbersome
  Small number of crashes, especially severe or injury crashes
  Further data typically cannot be collected after initial data collection is complete

## Slide 22: Barriers in CMV naturalistic data
Event-based data barriers
  Data are typically proprietary and require data use license or more
  Driver variables are almost non-existent, and vehicle variables are limited
  Fleets determine the thresholds for events or what events are recorded
  Typically limited in event-reduction variables
  Non-crash events may be limited in utility
  Wide variety of technologies lead to in-depth analysis of capabilities before and during analysis

## Slide 23: Special Considerations for CMV naturalistic data
Continuous and event-based data special considerations
  Fleets that adopt onboard technologies are typically more safety-minded
  Attaining owner-operator or independent drivers is difficult, and these drivers collectively have higher crash rates
  Automated technologies may influence how drivers behave, but the presence of these technologies on vehicles is not always captured in data collections