## Slide 1: Aging and Driving

## Slide 2: Seniors & Driving

## Slide 3: Seniors: Population Projection in US
U.S. Population Aged 65 and Older from 2016-2060 (in thousands)
Chart: Year
| 2016 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050 | 2055 | 2060
.65 years and over | 49244 | 56052 | 65226 | 73138 | 77997 | 80827 | 82835 | 85675 | 89615 | 94676
U.S. Population Aged 65 and Older Composition from 2016-2060 (in percent)
Data source from US Census Bureau, Projections for the United States: 2017 to 2060
Chart: Year
| 2016 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050 | 2055 | 2060
.65 years and over | 15.24 | 16.85 | 18.96 | 20.61 | 21.4 | 21.66 | 21.75 | 22.06 | 22.64 | 23.45

## Slide 4: Senior: Licensed Driver Projection in US
Average Percentage of Senior Licensed Drivers aged 65 and over
Chart: YEAR
| 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
Avg. % of Total Licensed Driver | 0.029 | 0.029 | 0.03 | 0.03 | 0.031 | 0.031 | 0.032 | 0.033 | 0.034 | 0.035 | 0.036
Average Number of Licensed Senior Drivers aged 65 and over
Chart: year
| 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
Avg. Number of Licensed Driver | 5795243.4 | 5868254.6 | 6027093.2 | 6209065.4 | 6447650.4 | 6586966.4 | 6746323.6 | 6913189.35 | 7188866 | 7366043.2 | 7689637.4

## Slide 5: Seniors: Crash Rate
The rate of passenger vehicle fatal crashes per 100 million miles driven began to increase at the age group of 65-69. Drivers aged 85 and older had the highest rate of fatal crash involvement.
(Rate=No. of crash involvement/ miles driven*100000000)
Data source is from IIHS, retrieved from
http://www.iihs.org/iihs/topics/t/older-drivers/fatalityfacts/older-people#cite-text-0-2 )
Chart: passenger vehicle fatal crash involvements per 100 million miles traveled by driver age, 2008
| 16-19 | 20-24 | 25-29 | 30-34 | 35-39 | 40-44 | 45-49 | 50-54 | 55-59 | 60-64 | 65-69 | 70-74 | 75-79 | 80-84 | ≥85
 | 4.6 | 3.8 | 3.6 | 1.8 | 1.3 | 1 | 1.4 | 1.2 | 1.1 | 1.2 | 1.4 | 2.1 | 2.7 | 4.2 | 8.8

## Slide 6: Seniors: Vehicle Crash Trend
Retrieved from IIHS: http://www.iihs.org/iihs/topics/t/older-drivers/fatalityfacts/older-people#cite-text-0-2
Motor Vehicle Crash Deaths and Deaths per 100,000 people 70 and older from 1975 to 2016
Notes: A total of 4,792 people ages 70 and older died in motor vehicle crashes in 2016. This is 18 percent fewer than in 1997, when deaths peaked, but a 27 percent increase since 1975. Deaths of older people increased 8 percent from 2015 to 2016. The rate of fatalities per capita among older people has decreased 43 percent since 1975.

## Slide 7: Age-related Declines: Vision
Age-related Declines | Driving problems
Declines in night vision, declines in dark adaptation ability and needs longer glare recovery time. | Have difficulty seeing other road users or traffic signs while driving at night, and difficulty seeing after having on-coming cars’ headlights flashed at night.
Reduced motion perception and difficulty in perceiving motion in depth, including judging speed and distance of other road user. | Difficulty in judging relative speeds of other road users and perceiving the traffic situation.
Declines in visual acuity | Hard to read the road signs in the moving vehicle
Declines in eye movements ability, also declines the maximum extent of gaze without head movement | Difficulty in locating objects and resolving the details of objects that are in motion; Hard to read the dashboard and simultaneously look on the road without a head movement.
Reduced Useful Field View (UFOV) | Difficulty in detecting objects or other road uses in peripheral visual field.

## Slide 8: Age-related Declines: Cognition
Age-related Declines | Driving problems
Decreased attentional ability | Higher crash risk when engaging in non-driving secondary tasks, difficulty in identifying hazards when driving.
The duration of short term memory(STM) is shorter and STM processing speeds are significantly longer. | Driving slowly and hesitantly, with unexpected maneuvers, longer time to deal with potential hazard situations.
Difficulty in transmitting and retrieving information from long term memory (LTM) | Difficulty in remembering what to do in certain driving situations and recalling and complying with driving laws. Easier to get lost. Difficulty in navigating and finding locations.
Declines in spatial cognition ability, including cognitive mapping ability and navigation ability. | Difficulty in navigating and finding locations.
Increased reaction time | Late response to changing driving conditions, slow to respond to road and traffic signs, slow to respond to hazards

## Slide 9: Age-related Declines: Psychomotor Skills
Age-related Declines | Driving problems
Less joint flexibility and limited range of motion, declined ability to rotate the head | Failure to scan the rear, back up, and turn the head to observe blind spots. Reverse parking can be difficult
Declines in strength | Failure to brake
Increased frailty | Reduced tolerance to injury in the event of a crash
Increased susceptibility to fatigue | Easy to be fatigued on long journeys

## Slide 10: Summary
U.S. population is aging
U.S. senior drivers are increasing
Crash rate increases for those over 70 years old
Age-related decline may contribute to higher driving risks
  Vision
  Cognition
  Motor control

## Slide 11: Advanced Driver Assistance System (ADAS)
Notes: Nathan, I think we should stick w/ “ADAS” to avoid confusion w/ our data acquisition system (DAS) – I’ve made this correction throughout the deck – thx.

## Slide 12: Advanced Driver Assistance System (ADAS)
Warning and crash mitigation
  Blind Spot Detection
  Forward Collision Warning and Braking
  Lane Departure Warning
  Lane Keeping Assistance
Visibility
  Advanced Forward Lighting Systems
  Backing Aids
  Night Vision Systems
  Pedestrian Detection
Vehicle Control
  Roll Stability Control
  Traction Control
Other driver assistance
  Adaptive Cruise Control
  Brake Assist
  Driver Monitoring
  Speed Alert
  Tire Pressure Monitors
  The category is based on Transport Canada (2013), retrieved from https://www.tc.gc.ca/eng/motorvehiclesafety/safevehicles-vehicle-safety-related-technologies-1068.htm

## Slide 13: Advanced Driver Assistance System (ADAS)
 | Functionality
Adaptive Cruise Control | Keeps a set speed or a set following distance relative to a leading vehicle
Lane Keep Assist | Steers back into the lane when detects drifting out of it
Lane Departure Alert | Sends alert when detects drift
Blind Spot Warning | Indication that vehicles are located in the blind spot; warning if collision is imminent

## Slide 14
Function | Description
Adaptive Cruise Control (ACC) | ACC is designed to assist the driver by maintaining a set speed or a set distance to the vehicle ahead. ACC uses radar sensors to monitor the distance between the head vehicle, and drivers can take over anytime through braking. ACC stops the vehicle at a comfortable distance from the head vehicle with no extra alerts provided.
Blind Spot alert | Blind spot alert system is designed to warn drivers when it detects other road users present at the areas directly alongside and behind the car (blind spot area). Blind spot alert system uses seniors monitoring blind spot areas, once activated, it alerts drivers through visual, acoustic or tactical signals.
Lane Keeping Assist (LKA) | Lane keeping assist is designed to assist drivers return to their lanes if it detects the vehicle drifting from their lane. LKA shares the information provided by the camera with the lane departure warning (LDW) system to determine the lateral location of the vehicle with respect to the lane boundary, once activated, LKA steers the vehicle back to the lane, at the same time, it alerts drivers through visual, acoustic or tactical signals.
Lane Departure Warning (LDW) | LDW is designed to alert drivers when it detects the vehicle unintentionally drifting out of its lane without a turn signal. Not like LKA, LDW does not control the vehicle. Instead of warning the driver to steer the vehicle back to the lane. LDW uses a camera to monitor the distance between the vehicle and the clear lane markings, once it detects the drifting, it informs drivers through visual, acoustic, or/and tactical warnings.

## Slide 15: Research to Reduce Driving Risks
ADAS has potential to assist senior drivers by compensating for age-related declines
Two key questions:
  Will seniors improve their driving with ADAS?
    Driving performance and safety may be different from the design expectation
  Will seniors accept and thus use new technology/ADAS?
    Less interest in the vehicle technologies than youngers
    Less willingness to spend on these technologies than youngers
    Less likely to embrace the concept of driverless cars
    Showed concerns about riding in self-driving vehicles

## Slide 16: Senior Mixec Level of Automation Experiment (SMX)
18 participants (70-79) drove study vehicles with mixed-level automated vehicle systems and equipped with DAS for six weeks
Pre-study survey on automated features
Vehicle orientation and vehicle training
Driving with the loaner vehicle with mixed level automated features and DAS
Focus group
Weekly phone interview
After-study survey on automated features
Initial attitudes towards automated features
Experienced attitudes towards automated features
Discussion on attitudes, perception and experience
Usage and attitudes
towards automated features each week
Driving behavior recorded by camera
Driving data and vehicle data recorded by sensors

## Slide 17
Brands | Vehicle | Blind Spot Warning | Lane Departure Alert | Adaptive Cruise Control | Lane Keep Assist
Audi |  | On automatically, can adjust brightness | Have to activate (40+ mph), steering, visual, and vibration | On automatically with cruise control, also automatic low-speed ACC | Have to activate (40+ mph) - visual, vibration, steering
 |  |  |  |  | On automatically if cruise control is on (37+ mph) -visual, vibration and steering (and directional braking)
Mercedes |  | On automatically | On automatically (37+ mph), visual and vibration |  | 
Volvo |  | On automatically | On automatically (30+ mph) |  | On automatically (30+ mph) – visual
 |  |  |  |  | Have to activate- chime, visual and steering input- can be set to high/low intervention
Infinity |  | On automatically, can adjust brightness | On automatically, chimes and visual |  | 
Notes: Operate over 37

## Slide 18: Senior Driving Performance with ADAS

## Slide 19: Study 1 - Objective
Examine how senior drivers use ADAS in naturalistic driving settings
  ADAS might encourage seniors to drive more, thereby improving mobility
  ADAS might improve driving performance, thereby improving safety

## Slide 20: SMX Study
18 participants (70-79) drove study vehicles with mixed-level automated vehicle systems and equipped with data acquisition system (DAS) for six weeks
Pre-study survey on automated features
Vehicle orientation and vehicle training
Driving with the loaner vehicle with mixed level automated features and DAS
Focus group
Weekly phone interview
After-study survey on automated features
Initial attitudes towards automated features
Experienced attitudes towards automated features
Discussion on attitudes, perception and experience
Usage and attitudes
towards automated features each week
Driving behavior recorded by camera
Driving data and vehicle data recorded by sensors

## Slide 21: Comparison between SHRP2 vs SMX
The influence on seniors’ driving was assessed through comparison between the two datasets:
  Examining Senior Drivers’ Adaptation on Mixer Automated Vehicle Technologies (SMX)
  Seniors recruited at State College, Pennsylvania in the Second Strategic Highway Research Program Naturalistic Driving Study (SHRP 2 NDS)

## Slide 22: SHRP2 vs SMX Participants
SHRP2 | SMX
N=Over 3500 | N=18
Location: Bloomington, IN; State College, PA; Tampa Bay, FL; Buffalo, NY; Durham, NC; Seattle, WA | Location: Blacksburg, VA
Participated in study 1-2 years | Participated in study 6 weeks
Age 16-98 | Age 70-79
Participant’s provided his/her owned vehicle as study vehicle | VTTI provided study vehicle and loaned to participants

## Slide 23: Selection of SHRP 2 Data Subset
State College, PA and Blacksburg, VA share similar demographics
  Dominated by students, employees and retirees from Pennsylvania State University and Virginia Tech
  Economic activities mainly caters college life.
 | State College, PA | Blacksburg, VA
Population | 42,352 | 44,678
Percentage of persons 65 years and over | 5.5% | 5.5%
Number of households | 12,523 | 13,436
Bachelor’s degree or higher, percentage of persons age 25 years and over | 70.4% | 70.9%
Mean travel time to work (minutes), workers age 16 + | 15.4 | 14.6
Top employer | PSU | VT

## Slide 24: Final Comparison Samples
 | SHRP 2 _PENN | SMX
Participant Subsets | N=30 (Male=16, Female=14) | N=18 (Male=9, Female=9)
Age Groups | Range=70–79, Mean=74.43, SD=3.45 | Range=70–79, Mean=74.00, SD=2.85
Recruitment Sites | State College, Pennsylvania | Blacksburg, Virginia
Total Trips Available for Analysis | 43,314 39,542 after removing invalid trips* | 2,118 1,983 after removing invalid trips
Study Duration per Participant | Mean=88.57 weeks, SD= 35.32, range=16.99 to 140.14 weeks | 6 weeks
Kilometers Traveled | 376,292.98 | 23,026.35
* Invalid trip: the trips with mean speed in km/h = 0 / NA, distance in km = 0 / NA, or start hour = NA.
Table. SHRP 2_PENN and SMX Data Subsets

## Slide 25: SMX and SHRP 2 –Data
Vehicle Data
  Acceleration data (3 axis)
  Rate sensors (3 axis)
  Turn signals
  GPS: latitude longitudinal, elevation, time, velocity
  Vehicle network data
    Accelerator, Brake pedal activation, Gear position, Steering wheel angle, etc.
Forward view (upper left), the driver’s face (upper right), downward view of the instrument panel and the driver (lower left), foot on the brake (lower left), and rear view (lower left)
Dashboard views of Audi( upper left), Infinity (upper right), Mercedes (lower left) and Volvo (lower right)

## Slide 26: Mobility Analysis
How does driving with an ADAS-equipped vehicle influence the types of trips driven by seniors (e.g., when they drive, how long they drive)?
Mobility was evaluated by comparisons between SHRP2 vs SMX in terms of:
  Overall driving exposure, and
  Driving patterns to answer the research question:
Driving exposure | Driving pattern
Number of trips per week Distance driven per week | Percentage of trips during nighttime Percentage of trips during rush hour traffic Percentage of long-distance trips Percentage of trips on high-speed roads

## Slide 27: Mobility Results
Mobility Analysis Statistical Results (Sample Size: 30 for SHRP 2_PENN, 18 for SMX)
Note: T = Welch’s t-test; U = Mann-Whitney-Wilcoxon test
Measure | Test Statistics | Degrees of Freedom | P-Value
Number of trips/week | T = −0.23 | 44 | 0.59
Distance driven (km)/week | T = 1.34 | 38 | 0.09
Percentage of trips during rush hours | T = 0.98 | 29 | 0.17
Percentage of night trips | U = 351.50 | - | 0.97
Percentage of long-distance trips | U = 440.00 | - | 0.51
Percentage of trips on high-speed roads | T = 0.98 | 37 | 0.17
Mobility of the two populations driving two different types of cars showed no significant differences.

## Slide 28: Mobility
Mobility of the two populations driving two different types of cars showed no significant differences.
  New technology requires adaptation time
  Commuting and traveling patterns cannot change either by choice or circumstances (e.g., economy, work, etc…)
    Seniors who participated in the both groups were healthy and capable of driving, with no restrictions voluntarily being added.

## Slide 29: Driving Performance Analysis
How does driving with an ADAS-equipped vehicle influence seniors’ driving performance?
  Comparisons also made between trips using and not using ACC within SMX study
Driving performance was evaluated by comparisons between SHRP2 vs SMX, or within SMX in terms of:
  Lateral acceleration events and magnitudes
  Longitudinal acceleration events and magnitudes
Lateral acceleration | Lateral acceleration
Number of lateral events/km Variance in acceleration magnitudes across lateral events | Number of longitudinal acceleration events/km Number of longitudinal deceleration events/km Variance in acceleration/deceleration magnitudes across longitudinal events

## Slide 30: Driving Performance Results
Driving Performance: SHRP 2_PENN vs. SMX (Sample Size: 30 for SHRP 2_PENN, 18 for SMX)
T = Welch’s t-test; U = Mann-Whitney-Wilcoxon test
Measure | Test Statistics | Degrees of Freedom | P-Value
Number of lateral events/km | T = −1.74 | 28.88 | 0.09
Variance in acceleration magnitudes across lateral events | T = 24.49 | 32.15 | <.001
Number of longitudinal acceleration events/km | U = 106 | - | <.001
Number of longitudinal deceleration events/km | U = 412 | - | 0.002
Variance in acceleration/deceleration magnitudes across longitudinal events | T = 4.19 | 29.80 | <.001

## Slide 31: Performance Results
Variance in acceleration magnitudes across lateral events (left) and number of longitudinal acceleration events/km (right) of SHRP 2_PENN and SMX.

## Slide 32: Performance Results
Number of longitudinal deceleration events/km (left) and variance in acceleration/deceleration magnitudes across longitudinal events (right) of SHRP 2_PENN and SMX.

## Slide 33: Driving Performance
Smaller variance in acceleration magnitudes across lateral events - More stability and better lateral control performance for seniors driving the ADAS-equipped vehicles.
Smaller variance in acceleration/deceleration magnitude across longitudinal events - ADAS may help seniors better manage their speed, for example, reducing hard braking, which can help with headway management.

## Slide 34: Limitations
Extraneous factors - road and traffic environment, traffic volume, weather, traffic laws at the data collection sites (nature of naturalistic driving study)
Study vehicles – participants drove new and unfamiliar cars (SMX) vs. their own cars (SHRP2)
Representativeness – participants were healthy and active drivers, considering that they actively participated in the driving study

## Slide 35: Senior Attitudes on ADAS

## Slide 36: Study 2 – Objective
Examine how senior drivers change their attitudes towards automated features based on actual use
  Acceptance of seniors is necessary to realize benefits of these technologies
  Seniors found to accept new technologies differently and may take longer to adapt to new technologies

## Slide 37: SMX Study
18 participants (70-79) drove study vehicles with mixed-level automated vehicle systems and equipped with data acquisition system (DAS) for six weeks
Pre-study survey on automated features
Vehicle orientation and vehicle training
Driving with the loaner vehicle with mixed level automated features and DAS
Focus group
Weekly phone interview
After-study survey on automated features
Initial attitudes towards automated features
Experienced attitudes towards automated features
Discussion on attitudes, perception and experience
Usage and attitudes
towards automated features each week
Driving behavior recorded by camera
Driving data and vehicle data recorded by sensors

## Slide 38: Focus Group
Location: Virginia Tech Transportation Institute, Blacksburg, VA
Length: 90-minute session
Experimenters: One facilitator, two observers
Participants: Six participants per session
(total of 3 sessions)
Notes: 6 per session

## Slide 39: Focus Group Probe Topics & Questions
Topics |  | Probe Questions
Attitudes | Q1. | What one word describes how you felt about the advanced features in your vehicle when you began the study? What one word describes how you feel about the advanced features in your vehicle now, at the end of the study?
 | Q2. | What caused your feelings to change or remain the same?
Perception | Q3. | What would make you feel more comfortable with these features?
Feature Likes/Dislikes | Q4. | What is one thing you liked best about these features? What is one thing you liked least about the features?
Safety | Q5. | Suppose a friend is considering purchasing a car with these features and they ask you if you think if they improve driving safety or not. What would you say?

## Slide 40: Shift in Attitude (Valence)
Negative initial attitudes towards the advanced features
  e.g. “Nervous”, “confused” and “anxious”
Positive post attitudes towards the advanced features
  e.g. “Positive” and “Confident”
Attitudes Change
Notes: start of study

## Slide 41: Design
More intuitive control
    Intuitive placement of the control
        “I think the display could be much more intuitive”
    Touchscreen
        “So the screen was not a dedicated screen to control”
        “when you were touching the screen, it didn’t always recognize you were touching the screen”

## Slide 42: Most Liked Feature – Blind Spot Alert
Improves visibility
  “that mirror (blind spot alert) told you there was something there you need to see”
Increases confidence
  “It did increase my confidence in driving. In traffic, I’d like to have that.”
Least intrusive
  “It is the least intrusive on everything else. It’s there, it doesn’t hurt anything.”

## Slide 43: Least Liked Feature – Lane Keeping Assist
Lack of trust
  “I felt like I couldn’t trust it” “Cause sometimes worked, sometimes didn’t”
Too many limitations
  “It didn’t work well in bad weather”
  “The limitations of that system made it something that I wouldn’t want to have”
  “if it doesn’t have that painted line, it won’t see anything”

## Slide 44: Safety Concerns
Most agreed that the features improve safety
  Learning how to use first: “Learn first then buy”
  Do not become over dependent on them: “Don’t get complacent”

## Slide 45: Training and Experience
Usage improved attitude
  “I think practice made the awkward just go away”
Reading manual improved attitude
“The manual I have outlined the limitations very clearly, so all of that made me feel … better about the system”
Better training
    Content: include operations of non-safety features (radio, GPS)
    Trainer: car dealers, family members, and/or friends
    Method: Re-orientation session after week or two into driving

## Slide 46: Summary of Focus Group Findings
 | Findings | Sample Response
1 | Negative initial attitudes towards the advanced features | “Anxious” “Nervous” “Unsure”
2 | Positive post attitudes towards the advanced features | “Confident” “Satisfied” “Convinced”
3 | Usage experience improved attitude | “I think practice made the awkward just go away”
4 | Reading manual improved attitude | “The manual I have outlined the limitations very clearly, so all of that made me feel … better about the system”
5 | Expected better training | “I would appreciate being able to go back and have somebody to ride with me, not just explain it, see how I am using it to the best advantage of how I drive”

## Slide 47: Summary of Focus Group Findings
 | Findings | Sample Response
6 | Expected more intuitive control | -Placement of the control “I think display could be much more intuitive” -Touchscreen “So the screen was not a dedicated screen to control”
7 | Liked best blind spot alert | “It did increase my confidence in driving, in traffic. I’d like to have that”
8 | Like least lane keeping assist | “I couldn’t trust it” “Sometimes worked, sometimes didn’t”
9 | Agreed that the features improve the safety | -Learning how to use first “Yes, there is a learning curve” -Do not become over dependent on them “Don’t get complacent”

## Slide 48: Thank you!